## Slide 1: Brain Computer Interaction
Course Instructors
Dr. Sreeja S R
Assistant Professor
Indian Institute of Information Technology
IIIT Sri City
Feature Extraction

## Slide 2: Features
The purpose of a BCI is to detect and quantify characteristics of brain signals that indicate what the user wants the BCI to do, to translate these measurements in real time into the desired device commands, and to provide concurrent feedback to the user.
The brain-signal characteristics used for this purpose are called signal features, or simply features.
Feature extraction is the process of distinguishing the pertinent signal characteristics from extraneous content and representing them in a compact and/or meaningful form, amenable to interpretation by a human or computer.

## Slide 3: Overall structure of a BCI

## Slide 4: Feature vector
A fundamental signal feature is simply a direct measurement of the signal. They usually provide limited relevant information about typically complex brain signals.
Thus, it is more common for BCIs to use features that are linear or nonlinear combinations, ratios, statistical measures, or other transformations of multiple fundamental features detected at multiple electrodes and/or multiple time points.
Such complex features, if selected appropriately, can reflect the user’s desires more accurately than the fundamental features themselves.
Most features used in BCI applications are based on spatial, temporal, and/or spectral analyses of brain signals or the relationships among them.
Furthermore, in order to determine the user’s wishes as accurately as possible, most BCIs extract a number of features simultaneously. This set of features is referred to as a feature vector.

## Slide 5: Feature vector
To be effective for BCI applications, a feature should have the following attributes:
its spatial, temporal, spectral characteristics, and dynamics can be precisely characterized for an individual user or population of users
it can be modulated by the user and used in combination with other features to reliably convey the user’s intent
its correlation with the user’s intent is stable over time and/or can be tracked in a consistent and reliable manner

## Slide 6: BCI SIGNAL PROCESSING - Fourier Analysis
Much of signal-processing theory is rooted in Fourier analysis, which transforms a time-domain (i.e., time on the x-axis) signal into its equivalent frequency-domain (i.e., frequency on the -axis) representation.
The primary utility of Fourier analysis is to decompose a signal into individual sinusoidal components that can be isolated and evaluated independently.
Using Fourier analysis, practically any signal can be accurately represented as the sum of a number (possibly an infinite number) of amplitude-scaled and time-shifted sinusoids at specific frequencies.
In order to model these signals, it is necessary to properly adjust the phase and the magnitude of each sinusoid.

## Slide 7: Fourier Analysis
For an arbitrary signal x(t), the magnitude (scale) and phase (shift) of the sinusoid at each frequency [ω(radians) = 2πf (Hz)] required to represent an arbitrary signal can be determined from the Fourier transform:
The magnitude and phase for each sinusoidal component are given as:

## Slide 8: THE THREE STEPS OF FEATURE EXTRACTION
The process of feature extraction is discussed here as a three-step procedure:
signal conditioning to reduce noise and to enhance relevant aspects of the signals
extraction of the features from the conditioned signals
feature conditioning to properly prepare the feature vector for the feature-translation stage

## Slide 9: FIRST STEP: SIGNAL CONDITIONING
The first step of feature extraction is called signal conditioning or preprocessing.
This step enhances the signal by preemptively eliminating known interference (i.e., artifacts) or irrelevant information, and/or by enhancing spatial, spectral, or temporal characteristics of the signal that are particularly relevant to the application.
It is common to have some prior knowledge about the general signal characteristics relevant for a particular application, and this knowledge is used in conditioning.

## Slide 10: FIRST STEP: SIGNAL CONDITIONING
Signal conditioning can include a number of different procedures that can primarily be categorized as:
  frequency-range prefiltering
  data transformation and normalization
  spatial filtering
    Data independent spatial filtering (common- average reference and surface Laplacian spatial filters)
    Data dependent spatial filtering (PCA, ICA and CSP)
  removal of environmental interference and biological artifacts

## Slide 11: Frequency-Range prefiltering
Digital filters are central to digital signal processing. They modify the frequency content of a digital signal by attenuating some frequencies (or frequency ranges) and amplifying others. Each successive sample of a digitized signal is passed through a digital filter to produce a new value as the output.
  Low pass filter (higher frequencies are attenuated and lower frequencies are preserved)
  High pass filter (very specific ranges of signal frequencies can be amplified, attenuated, preserved, and/or eliminated)
  Bandpass filter (A band-pass filter preserves signal power within a specified continuous frequency range, while attenuating signal power outside of this range)
  Notch filter/Band-stop filter (A notch filter is the converse of a bandpass filter; it attenuates signal power within a specified continuous frequency range, while preserving signal power outside of this range)

## Slide 12: Data Transformation
Data transformation are needed to bring uniformity to the data. In addition, it can be used to scale the data to a preferred range. Following are few methods as data transformation.
Change of origin
Change of scale
Change of origin and scale
Decimal scaling
Min-Max normalization
Standard normalization

## Slide 13: Data Transformation
1. Change of Origin:
Arbitrarily choose a constant. If sample values are integers, an integer constant is preferred.
Shift data point by subtracting (or adding) the chosen constant from each sample observation.
This technique is useful when data values are large, and variability is not so large.
Lemma 6.1:
The range of original data is preserved by a change of origin transformation.
If is the old mean and is the chosen constant, then the new mean of the transformed data is

## Slide 14: Data Transformation
Example:
Apply change of origin method to the following data and calculate the old and new means.
Let us arbitrarily chose the constant 120 and subtract this from each value in to get the transformed data as
The new mean
The mean of the original data is

## Slide 15: Data Transformation
2. Change of scale:
This method is used to shorten the range of large numbers or lengthen the range of very small numbers.
Chose (arbitrarily) a non-zero constant . If is less then the minimum of the observation, each value will be transformed to a value greater than 1. On the other hand, if it is greater than the maximum of the observation, then each value will be transformed to a value less than 1.
If the value is between min and max of the sample, then the transformed values lie on the real line (positive real line if all ’s are positive)
If all values are small fractions, we may multiply a large constant to scale them up and vice-versa.

## Slide 16: Data Transformation
3. Change of origin and scale:
This is the most frequently used method to standardize data values. Depending upon the constants used to change the origin and scale, a variety of transformation intervals can be obtained.
Example: A sample in the range (a, b) can be transformed to a new interval (c, d) by the following transformation.
Let is the original and is the transformed value. Then
[Prove that all values in the range (a, b) are mapped onto the range (c, d)].

## Slide 17: Data Transformation
4. Min-Max Normalization:
Min-Max normalization performs a linear transformation on the original data.
Suppose, and are the minimum and maximum values of an attribute . Min-Max normalization maps a value, of to in the range and using the following transformation:
If [ , then it is a special case of Min-max normalization.

## Slide 18: Data Transformation
5. Standard Normalization:
This transformation is so called because it is extensively used in statistics in standardizing normal scores.
Here, the origin is changed using the mean of the sample, and the scale is changed using the standard deviation of the sample.
where and are the mean and std for the attribute A.
This method is also alternatively termed as z-score normalization (zero-mean normalization) and the transformed values are called z-scores.

## Slide 19: Data Transformation
5. Standard Normalization:
Example: Given X = {32, 80, 56, 75, 69, 26, 44, 50}. Apply the standard normalization.
Here, the mean 390. Thus the z-scores are
= {-1.1140133 1.3165612 0.1012739 1.0633763 0.7595545 -1.4178351 -0.5063697 -0.2025479}
Note: It is very interesting to note that z-scores will always lie in the interval [-3, +3]

## Slide 20: Data Transformation
6. Decimal Scaling:
This data transformation method is same as the “change of scale” method by either scale up or scale down.
Here j represents movement of decimal points. Decided based on the maximum value in the data.

## Slide 21: SECOND STEP: EXTRACTING THE FEATURES
BLOCK PROCESSING
  For most BCI applications, it is highly desirable for the processing to occur in real time. Prior to feature extraction, the incoming signal samples are commonly segmented into consecutive, possibly overlapping, sample blocks.
  A feature vector is created from the signal samples within each individual sample block. The feature vectors from the successive sample blocks are then fed to the translation algorithm, which produces a device command or user feedback corresponding to each sample block or corresponding to sets of consecutive sample blocks.
  For efficient online implementation, the length and overlap of these sample blocks should fit the relevant temporal dynamics of the signal, the feature-extraction method, the nature of the application, and the concurrent user feedback, as well as the available processing power.
    E.g., BCI cursor control
    P300 response

## Slide 22: SECOND STEP: EXTRACTING THE FEATURES
TIME (TEMPORAL) FEATURES
Peak-Picking and Integration
  Peak-picking simply determines the minimum or maximum value of the signal samples in a specific time block (usually defined relative to a specific preceding stimulus) and uses that value (and possibly its time of occurrence) as the feature(s) for that time block.
  The signal can be averaged or integrated over all or part of the time block to yield the feature(s) for the block. Some form of averaging or integration is typically preferable to simple peak-picking, especially when the responses to the stimulus are known to vary in latency and/or when unrelated higher-frequency activity is superimposed on the relevant feature

## Slide 23: SECOND STEP: EXTRACTING THE FEATURES
TIME (TEMPORAL) FEATURES
Correlation and Template-Matching
  The similarity of a response to a predefined template might also be used as a feature.

## Slide 24: SECOND STEP: EXTRACTING THE FEATURES
Statistical features
Sl. No | Features | Short description
1 | MEAN | Mean value
2 | STD | Standard deviation
3 | MAX VALUE | Maximum positive amplitudes
4 | MIN VALUE | Maximum negative amplitudes
5 | SKEWNESS | a measure of asymmetry of the distribution
6 | KURTOSIS | a measure of flatness of the distribution
7 | MEDIAN | the middle value of a set of ordered data

## Slide 25: SECOND STEP: EXTRACTING THE FEATURES
Interval or period analysis features.
Sl. No | Features | Short description
8 | LINE LENGTH | Line length
9 | MEAN VV AMPL | Mean of vertex-to-vertex amplitudes
10 | VAR VV AMPL | Variance of vertex-to-vertex amplitudes
11 | MEAN VV TIME | Mean of vertex-to-vertex times
12 | VAR VV TIME | Variance of vertex-to-vertex times
13 | MEAN VV SLOPE | Mean of vertex-to-vertex slope
14 | VAR VV SLOPE | Variance of vertex-to-vertex slope
15 | ZERO CROSSING | Number of zero crossings in a signal
16 | MIN MAX NUMBER | Number of local minima and maxima
17 | COEFF OF VARIATION | a statistical measure of the deviation of a variable from its mean, standard deviation divided by mean
18 | AMPL RANGE | The difference between the maximum positive and maximum negative Amplitude values

## Slide 26: SECOND STEP: EXTRACTING THE FEATURES
Features derived from the first and second derivative.
Sl. No | Features | Short description
19 | 1st DIFF MEAN | Mean value of the first derivative of the signal
20 | 1st DIFF MAX | Maximum value of the first derivative of the signal
21 | 2nd DIFF MEAN | Mean value of the second derivative of the signal
22 | 2nd DIFF MAX | Maximum value of the second derivative of the signal

## Slide 27: SECOND STEP: EXTRACTING THE FEATURES
The Hjorth parameters
Sl. No | Features | Short description
23 | HJORTH 1 | Ability
24 | HJORTH 2 | Mobility (σx ′ /σx )
25 | HJORTH 3 | Complexity
Sl. No | Features | Short description
23 | HJORTH 1 | Ability
24 | HJORTH 2 | Mobility (σx ′ /σx )
25 | HJORTH 3 | 
NOTE:
σx ′ is the standard deviation of the first derivative of the signal
σx′′ is the standard deviation of the second derivative of the signal

## Slide 28: SECOND STEP: EXTRACTING THE FEATURES
FREQUENCY (SPECTRAL) FEATURES
Much brain activity manifests itself as continuous amplitude- and frequency-modulated oscillations. Therefore, it is often advantageous to accurately track these changes in the frequency domain. Although the Fourier transform is the most common method for converting from the time domain to the frequency domain, there are several alternatives that have characteristics that are particularly desirable given specific constraints or specific objectives. These include:
  band power
  fast Fourier transform (FFT)
  autoregressive (AR) modeling

## Slide 29: SECOND STEP: EXTRACTING THE FEATURES
FFT-based features calculated from the EEG spectra.
Sl. No | Features | Short description
26 | FFT DELTA | 0.1 - 3 Hz
27 | FFT THETA | 3 - 7 Hz
28 | FFT ALPHA | 7 - 12 Hz
29 | FFT BETA | 12 - 30 Hz
30 | FFT GAMMA | 30 - 40 Hz
31 | FFT WHOLE | 0.1 - 40 Hz

## Slide 30: SECOND STEP: EXTRACTING THE FEATURES
FFT-based Spectral Features.
Sl. No | Features | Short description
32 | FFT DT RATIO | DELTA / THETA
33 | FFT DA RATIO | DELTA / ALPHA
34 | FFT TA RATIO | THETA / ALPHA
35 | FFT DTA RATIO | (DELTA + THETA) / ALPHA
36 | FFT SEF | Spectral edge frequency (95 % of the total spectral power resides)
37 | FFT SP-ROLL OFF | The frequency below which 85 % of the total spectral power resides

## Slide 31: SECOND STEP: EXTRACTING THE FEATURES
Wavelet based Features.
Sl. No | Features | Short description
38 | MIN WAV VALUE | Minimum value
39 | MAX WAV VALUE | Maximum value
40 | MEAN WAV VALUE | Mean value
41 | MEDIAN WAV VALUE | Median value
42 | STD WAV VALUE | Standard deviation
43 | SKEWNESS WAV VALUE | Skewness
44 | KURTOSIS WAV VALUE | Kurtosis
45 | WAV BAND | Relative energy

## Slide 32: SECOND STEP: EXTRACTING THE FEATURES
Wavelet based Features.
Sl. No | Features | Short description
46 | ENTROPY SPECTRAL WAV | The spectral entropy
47 | 1st DIFF WAV MEAN | Mean value of the 1st derivative
48 | 1st DIFF WAV MAX | Maximum value of the 1st derivative
49 | 2nd DIFF WAV MEAN | Mean value of the 2nd derivative
50 | 2nd DIFF WAV MAX | Maximum value of the 2nd derivative
51 | ENERGY PERCENT WAV | Percentage of the total energy of a detail/approximation
52 | WAV ZERO CROSSING | Zero crossing
53 | WAV COEFF OF VARIATION | Coefficient of variation
54 | WAV TOTAL ENERGY | Total Energy

## Slide 33: SECOND STEP: EXTRACTING THE FEATURES
Other Features.
Sl. No | Features | Short description
55 | ENTROPY SPECTRAL | The spectral entropy
56 | ENTROPY SHANNON | The Shannon entropy
57 | MAX ABS XCORR EEG-EEG | Maximum positive amplitude of auto-correlation or cross-Correlation function
58 | MEAN ABS XCORR EEG-EEG | Mean value of auto-correlation or cross-correlation function

## Slide 34: THIRD STEP: FEATURE CONDITIONING
The distributions and the relationships among the features can have a significant effect on the performance of the translation algorithm that follows feature extraction. These effects depend on the characteristics of the particular translation algorithm.
  NORMALIZATION
  LOG-NORMAL TRANSFORMS
  FEATURE SMOOTHING
  PCA AND ICA

## Slide 35
Thank You!